## Slide 1: Simulation of ARM and x86 Using In-Order and Out-of-Order CPU Models with Gem5 Simulator
Presented By
Venkata Sasank Pamulapati, Anurag Kalagatoori, Sindhu Bhavana Mandala, Indrakiran Reddy Inapagundla

## Slide 2
Agenda
Introduction
Gem5 simulator and its key features
Building Gem5 simulator
Configurations
Commands used to run benchmarks
Performance metrics
Results and analysis
Conclusions
Challenges faced
Future work

## Slide 3
  In the past, Arm is mostly used for portable devices like mobiles and X86 is used for computers and Laptops and there is no much competition between them.
  But in the current period, since there is no limits between the performance of these devices, X86 and ARM became huge competitors.
  In this project, we compare both ARM and X86 architectures with both In-order and Out-of-order models by simulating Mi bench benchmark applications using Gem5 simulator.
Introduction

## Slide 4
Gem5 simulator and its key features
The Gem5 simulator is a modular platform for computer system architecture research, encompassing system-level architecture as well as processor microarchitecture.
There are two modes of execution:
1. System-Call Emulation (SE)
2. Full System Emulation (FS)
System-call emulation acts as a functional simulator with a console interface as a mean of communication to the user.
Full-system emulation allows user interaction with simulated operating system.
Here we use system-call emulation mode for simulation.

## Slide 5
Available binaries: gem5.opt, gem5.debug, gem5.prof, gem5.perf, gem5.fast.
Gem5.opt is used here and it has optimised build.
ISAs: ALPHA, ARM, MIPS, POWER, RISC-V, SPARC, x86.
Here we use ARM and X86 ISAs.
CPU Models: AtomicSimpleCPU, TimingSimpleCPU, HPI, MinorCPU, DerivO3CPU, O3_ARM_v7a_3, ex5_LITTLE, ex5_big, X86KvmCPU.
MinorCPU is used for In-order and DerivO3CPU is used for Out-of-order execution.
Memory Models: Classic, Ruby
Classic focuses on pipeline and Ruby focuses on memory hierarchy simulations.

## Slide 6
Tools used to build gem5:
    Git/Mercurial
    gcc/g++
    Python
    Scons
    Zlib
    M5
    ARM Cross Compiler(gnueabi)
Once downloaded gem5, go into the gem5 folder and build all the dependencies and then use this command to build gem5.
scons build/ <X86/ARM> /gem5.opt
Building gem5 Simulator

## Slide 7
  To simulate the performance of X86 and ARM architecture, gem5 needs to be run with the following configurations:
  1.In-order X86 architecture
  2.Out-of-order X86 architecture
  3.In-order ARM architecture
  4.Out-of-order ARM architecture
  For all the configurations we use different cache sizes and simulate the results
  System-call-emulation mode is used.(SE mode)
Configurations

## Slide 8
  ./build/X86/gem5.opt -d ~/qsort ./configs/example/se.py -c ./automotive/qsort/qsort_large --cpu-type=DerivO3CPU --caches --l2cache --l1d_size=32kB --l1i_size=32kB --l2_size=64kB --l1d_assoc=2 --l1i_assoc=2 --l2_assoc=8 --cacheline_size=64 –options=10 –o input_large.dat
  ./build/X86/gem5.opt -d ~/qsort ./configs/example/se.py -c ./automotive/qsort/qsort_large --cpu-type=MinorCPU --caches --l2cache --l1d_size=32kB --l1i_size=32kB --l2_size=64kB --l1d_assoc=2 --l1i_assoc=2 --l2_assoc=8 --cacheline_size=64 –options=10 –o input_large.dat
  ./build/ARM/gem5.opt -d ~/qsort ./configs/example/se.py -c ./automotive/qsort/qsort_large --cpu-type= DerivO3CPU --caches --l2cache --l1d_size=32kB --l1i_size=32kB --l2_size=64kB --l1d_assoc=2 --l1i_assoc=2 --l2_assoc=8 --cacheline_size=64 –options=10 –o input_large.dat
  ./build/ARM/gem5.opt -d ~/qsort ./configs/example/se.py -c ./automotive/qsort/qsort_large --cpu-type=MinorCPU --caches --l2cache --l1d_size=32kB --l1i_size=32kB --l2_size=64kB --l1d_assoc=2 --l1i_assoc=2 --l2_assoc=8 --cacheline_size=64 –options=10 –o input_large.dat
  while simulating for ARM architecture we need to cross compile the files and then simulate it.
Commands used

## Slide 9
To evaluate the performance of X86 and ARM we mainly use four performance metrics:
Throughput: It’s the amount of Information processed or transmitted in given amount of time.
Total Energy: It’s the amount of energy consumed to run the application.
Cache Miss Rate: The percentage of accesses that results in a miss is called cache miss rate.
Average CPI: The average number of cycles required to perform an instruction is called Cycles Per Instruction.
Performance Metrics

## Slide 10
Total Energy (pJ)
Chart: Qsort Benchmark
| Inorder L1=32k,L2=512k | Inorder L1=64k,L2=1M | Outoforder L1=32k,L2=64k | Outoforder L1=64k,L2=1M
ARM | 103264230345 | 99632574465 | 47853155280 | 42499620630
X86 | 207878318865 | 200421824475 | 71094908490 | 58301410980
qsort
Chart: Dijkstra Benchmark
| Inorder L1=32k,L2=512k | Inorder L1=64k,L2=1M | Outoforder L1=32k,L2=64k | Outoforder L1=64k,L2=1M
ARM | 55676047860 | 55113674565 | 27099306285 | 26825831655
X86 | 129692402985 | 126818916885 | 31230495135 | 29531991675
Chart: Basicmath Benchmark
| Inorder L1=32k,L2=512k | Inorder L1=64k,L2=1M | Outoforder L1=32k,L2=64k | Outoforder L1=64k,L2=1M
ARM | 639565612785 | 631060367805 | 465076945110 | 361664808870
X86 | 1553369114775 | 2443630000000 | 234713724735 | 233193234825
Chart: Bitcount Benchmark
| Inorder L1=32k,L2=512k | Inorder L1=64k,L2=1M | Outoforder L1=32k,L2=64k | Outoforder L1=64k,L2=1M
ARM | 47395245 | 47115510 | 24956325 | 25169580
X86 | 78781620 | 75818835 | 42611535 | 40587210

## Slide 11
Since the ARM architecture is simple, it consumes less energy than the X86 architecture.
Out-of-order model consumes less energy when compared to In-order model.
There's an exception in the Basic-math benchmark in out of order where x86 consumes less energy than ARM.
Total Energy(pJ)

## Slide 12
L2 cache miss rate
Chart: Basicmath Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 0.000464 | 0.00767 | 0.019 | 0.007
x86 | 6e-05 | 0.0684 | 0.009 | 0.1
Chart: Qsort Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 0.29564 | 0.22816 | 0.93055 | 0.37235
x86 | 0.51 | 0.403 | 0.92457 | 0.3454
Chart: Bitcount Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 0.56435 | 0.72945 | 0.67343 | 0.87747
x86 | 0.68949 | 0.91817 | 0.72451 | 0.95271
Chart: Dijkstra Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 0.006451 | 0.022658 | 0.006731 | 0.046314
x86 | 0.003468 | 0.047994 | 0.011251 | 0.15501

## Slide 13
From the results we can see that the L2 miss rates are higher for X86 architecture and lower for ARM architecture.
As the L2 cache is doubled, miss rates increase contrast to what we expect. This might be because of the System Emulation mode used in the simulator
L2 cache miss rate

## Slide 14
Throughput (bytes/sec)
Chart: Basicmath Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 111200 | 112746 | 576769 | 295246
x86 | 53692 | 53692 | 486782 | 232924
Chart: Qsort Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 76816968 | 88028673 | 428035408 | 114961774
x86 | 47909298 | 32478745 | 458986253 | 210912785
Chart: Bitcount Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 577965539 | 578762240 | 1012578240 | 1029750351
x86 | 531914970 | 558471322 | 993580068 | 1073056214
Chart: Dijkstras Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 893807 | 901712 | 2081320 | 2223425
x86 | 480524 | 491178 | 2142016 | 2090890

## Slide 15
The results show that the throughput is increasing when the CPU model is out-of-order.
During out-of-order, the number of instructions executed is high, and hence the throughput is high.
But X86 out of order performs well.
Throughput (bytes/sec)

## Slide 16
Average CPI
Chart: Basicmath Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 1.18 | 1.16 | 0.44 | 0.44
x86 | 2.98 | 2.98 | 0.9 | 0.7
Chart: Qsort Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 1.27 | 1.23 | 0.57 | 0.53
x86 | 2.83 | 2.75 | 0.9 | 0.77
Chart: Bitcount Benchmark
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 3.78 | 3.75 | 2.13 | 2.07
x86 | 6.87 | 6.62 | 3.54 | 3.31
Chart: DIJKSTRA
| in order 32-512 | in order 64-1 | out of order 32-64 | out of order 64-1
arm | 1.2 | 1.19 | 0.55 | 0.54
x86 | 2.87 | 2.81 | 0.68 | 0.65

## Slide 17
The results show that for all benchmarks the out-of-order CPU model has less CPI than in- order model.
ARM always has less CPI than x86. However, the difference between the two architectures when the CPU model is out-of-order is very small.
Average CPI

## Slide 18
  ARM outperforms X86 architecture in most cases
  X86 architecture is efficient when CPU model is out-of-order
  ARM is always more energy efficient than x86 except for the basicmath benchmark when the CPU model is out of order.
Conclusions

## Slide 19
Setting the environment for the gem5 simulator
Building the Gem5 simulator and solving the errors with installing various dependencies
While running quick sort and Dijkstra’s benchmarks, linking of the input file was required
Memory and performance issues while building on a Virtual Machine
Challenges Faced

## Slide 20
Simulation of ARM and X86 in Full System mode of Gem5 simulator
Compare both in-order and out-of-order performance of ARM and X86.
Evaluate architectures’ performance using other benchmarks.
Future Work

## Slide 21
References
Anas Ahmad Abudaqa, Talal M. Al-Kharoubi, Muhamed F. Mudawar, Armin Kobilica, Dept. of Computer Engineering, King Fahd University for Petroleum and Minerals, Dhahran, KSA, “Simulation of ARM and x86 microprocessors using in-order and out-of-order CPU models with Gem5 simulator”.
Nathan Binkert, Bradford Beckmann, Gabriel Black, Steven K. Reinhardt, Ali Saidi, Arkaprava Basu, Joel Hestness, Derek R. Hower, Tushar Krishna, Somayeh Sardashti, Rathijit Sen, Korey Sewell, Muhammad Shoaib, Nilay Vaish, Mark D. Hill, and David A. Wood, “The gem5 simulator”

## Slide 22
Individual Contributions
Team Member | Contributions
Indrakiran Reddy Inapagundla | Simulation and Evaluation of ARM architecture with In-order CPU model Collecting statistics for the same
Sindhu Bhavana Mandala | Simulation and Evaluation of X86 architecture with In-order CPU model Collecting statistics for the same
Venkata Sasank Pamulapati | Simulation and Evaluation of ARM architecture with Out-of-order CPU model Collecting statistics for the same
Anurag Kalagatoori | Simulation and Evaluation of X86 architecture with Out-of-order CPU model Collecting statistics for the same

## Slide 23
Thank You